## Slide 1: Graph Neural Network for Building Prediction Agents in Intent-Based Zero-Touch Networks
Department of Electrical Electronics and Computer Engineering, University of Ulsan, Ulsan, South Korea
1
Paper No: 20
Dangnachew Azene Temesgene | Elham Dehghan Biyar | Andrey Silva | Ankita Likhyani | András Zahernszky
Ericsson Research, Sweden | Ericsson Research, Turkey | Ericsson Research, Brazil | Ericsson GAIA, India | Ericsson Research, Sweden
Authors:
Presented By: UMAR MUHAMMAD
Student ID: 20245364
Date: 2025-11-27
Source: 2024 IEEE International Conference on Communications (ICC)

## Slide 2
Presentation Outline
  Part 1: Background and Motivation
    The Evolution: 5G → 6G Networks
    What are Intent-Based Networks?
    The Critical Problem: Conflict Detection
  Part 2: Related Work and Problem Context
  Part 3: Proposed GNN Framework
    Why Traditional Methods Fail
    Why Graph Neural Networks?
    GNN Architecture & Training
  Part 4: Experimental Setup and Results
  Part 5: Key Takeaways and Discussion
    Main Contributions
    Limitations and Future Work
2

## Slide 3
The Evolution of Network Management
4
4G (2010) | 5G (2020) | 5G-Adv (2024) | 6G (2030) | Future (2035+)
Manual Config
Partial Automation
Semi-Auto
Autonomous Operation
Fully Auto Zero-Touch
Complexity Explosion
4G Network:
1,000 base stations
100,000 parameters to configure
Human engineers: Manageable
6G Network (Projected):
10,000,000 connection points
100,000,000,000+ parameters
Human engineers: IMPOSSIBLE
THE CHALLENGE!
How do we manage networks that are too complex for human operators to configure manually?
ANSWER: Intent-Based Autonomous Networks

## Slide 4
What Are Intent-Based Networks?
Traditional (Configuration-Based)
Network Engineer specifies HOW:
↓
Set Router 1: QoS policy=7, bandwidth=50Mbps
Set Router 2: Priority=high, buffer=2048KB
Configure Switch 1: VLAN=105, MTU=9000
[... 50 more commands ...]
↓
Time: Hours to Days
Error Rate: 5-10% (human mistakes)
Scalability: Poor (limited by human capacity)
From Manual Commands to High-Level Intents
4
Manual Configuration | Intent-Based Network
Hundreds of CLI commands | Keep Latency < 60 ms
Reactive | Proactive and Predictive
Human-operated | Self-driving
A side-by-side comparison:
Intent-based (Goal-Based)
User specifies WHAT they want:
↓
"99% of URLLC users should experience maximum latency of 60ms and packet loss <1%"
↓
System automatically:
    - Translates intent → configurations
    - Configures all network elements
    - Monitors continuously
    - Adapts to changes
    - Resolves conflicts
↓
Time: Seconds to Minutes
Error Rate: <0.1% (automated)
Scalability: Excellent (handles millions)

## Slide 5
The Problem: Networks Are Becoming Too Complex
Modern networks = millions of parameters
  (traffic patterns, service requirements, topology changes)
Human configuration is no longer scalable
  → Too slow
  → Too error-prone
  → Too complex
Services are becoming diverse
  URLLC needs ultra-low latency
  Conversational video needs high QoE
  IoT devices need massive connectivity
Conflicts naturally appear
  Changing one setting may break another service's KPI
Future 6G vision
  → Autonomous, self-optimizing, self-healing networks
  → Operated not by commands, but by intents
Why Do We Need Intent-Based Zero-Touch Networks?
4
(a)
(b)
Fig. Tangled manual networks to clean, intent-driven network

## Slide 6: Problem Statement and Challenges
3
Why existing approaches are insufficient
Main Challenges
1. Complexity: Mathematical models (queuing theory, Markov chains) cannot capture dynamic network complexity [3].
2. Scalability: Traditional ML approaches (MLP, CNN) show poor generalization on large-scale networks.
3. Accuracy: Prediction agents must be fast, accurate, and scalable for run-time conflict detection.
4. Generalization: Models trained on one configuration should work on unseen topologies.
Research Question: Can Graph Neural Networks enable accurate, scalable, and generalizable prediction agents for intent-based networks?
Paper's Goal
Develop a GNN framework that predicts KPIs (specifically latency) for intent-based networks by learning from the underlying graph representation of the network environment.

## Slide 7
Related Work
GNN applications in network management
4
Work | Application | Key Contribution
RouteNet [10] | Delay Prediction | GNN recognizes topologies for per-path delay
Wang etal. [8] | Network Slicing | Virtual network representation, E2E metrics
STGCN [11] | SDN latency | Spatial-temporal forecasting in Abilene network
PERT-GNN [13] | Microservices | Latency prediction for resource allocation
Research Gap
No prior work focuses on automatic generation of prediction models for conflict detection in intent-based network management systems
Why GNNs?
Networks ARE graphs!
GNN Advantage
Native topology modeling

## Slide 8
Intent Manager Function: The Brain of Intent-Based Networks
The Intent Manager Function (IMF): How Intents Become Actions
4
Fig. Overview of the Intent Manager Function architecture.
LAYER 1: USER / SERVICE LAYER
  Users submit high-level intents in business language. Example: 'I want 99.9% availability' or 'I need low latency for video streaming.' These intents are passed to the IMF for translation into network configurations.
LAYER 2: INTENT MANAGEMENT FUNCTION (IMF) - THE INTELLIGENT CORE
  The IMF uses the MAPE-K control loop (Monitor, Analyze, Plan, Execute, Knowledge) to autonomously manage the network through continuous closed-loop operation:
  1. MONITOR (Data Grounding Agent):
    Collects KPIs from the network (throughput, latency, packet loss, resource utilization), processes real-time measurements, and compares them against intent targets.
  2. ANALYZE (Proposal Agent):
    Identifies root causes when intents are not fulfilled. Generates multiple possible corrective actions (e.g., increase bandwidth, change routing, reallocate resources). Passes proposals to Planning stage.
  3. PLAN (Prediction Agent) ← OUR PAPER'S CONTRIBUTION:
    Predicts the impact of each proposed action on ALL active intent KPIs. Detects potential conflicts (fixing one problem might violate other intents). Evaluates alternatives and selects the best action that optimizes overall performance without conflicts. This predictive capability enables truly autonomous zero-touch network operation.
  4. EXECUTE (Actuator Agent):
    Applies the selected configuration to network elements (routers, switches, base stations). Implements the chosen solution and loops back to Monitor stage to verify the outcome.
LAYER 3: NETWORK ELEMENTS LAYER
  Physical and virtual infrastructure (routers, switches, base stations, servers). Receives configuration commands from IMF and executes them. Sends monitoring data back to complete the feedback loop for continuous autonomous management.

## Slide 9
MAPE-K Control Loop with Prediction Agent
4
Step 1 - MONITOR: The monitoring agent measures network performance. Here, it found that URLLC latency is 75 milliseconds, but the target is less than 60 milliseconds. This violation triggers the next stage.
Step 2 - ANALYZE: The analysis agent identifies that CPU overload is causing the problem. It then generates three possible solutions: add more server replicas, move users closer to the edge, or increase the priority of URLLC traffic. These proposals go to the planning stage.
Step 3 - PLAN with Prediction Agent (OUR PAPER'S CONTRIBUTION): This is where the paper contribution comes in. The Prediction Agent uses Graph Neural Networks to predict what will happen if we implement each proposed action. It doesn't just look at URLLC latency it predicts the impact on ALL network services.
  For the first action, adding replicas: We predict the latency will drop to 55 milliseconds, which is good. But video quality will decrease to 4.3 out of 5, and it costs 840 dollars per month.
  For the second action, moving users to the edge: Latency improves to 45 milliseconds, video quality actually improves to 4.6 out of 5, and it only costs 120 dollars per month. This is clearly the best option.
  For the third action, increasing priority: Latency becomes 50 milliseconds, which meets our target. But video quality drops significantly to 3.8 out of 5. Even though this option is free, it creates a conflict with our video streaming requirements.
  The Prediction Agent selects the second action because it satisfies all requirements without creating new problems. This shows why prediction is critical—without it, we might choose the free option and unknowingly create video quality issues.
Step 4 - EXECUTE: The system now implements the selected action. It migrates five users to the edge server and monitors the results to confirm success.
Step 5 - KNOWLEDGE: The system stores this experience and updates its prediction models. This learning improves future decisions. The loop then returns to monitoring.
KEY INSIGHT: The Prediction Agent is the brain of autonomous networks. It evaluates all options before taking action, detects conflicts between different requirements, and selects the best overall solution. Without accurate prediction, the system would make decisions blindly and create new problems while trying to solve old ones.

## Slide 10
Why Graph Neural Networks?
Advantages over traditional approaches
4
Traditional Neural Networks
Graph Neural Networks
Fixed input size requirements
Cannot capture network topology
Poor scalability to larger networks
Limited Generalization
Require extensive training data
Variable graph size handling
Natural network representation
Excellent scalability
Superior generalization
Learn from graph structure
GNN Key Properties
Output does not depend on node ordering
Nodes exchange information with neighbors

## Slide 11
Data Collection: Network Emulator
Realistic test environment
4
Network Components
Two Services
UEs: User equipment (mobile devices)
gNB: 5G base station
UPF: User Plane Function
K8s Clusters: Central, Edge-1, Edge-2
User-plane probes: Traffic monitoring
URLLC Service
Request-response with computational tasks
WebRTC (CV)
Conversational video streaming
Configuration Details
Config | Airlink BW | WebRTC UEs | URLLC UEs | Delays (ms)
Config 1 | 10 Mbps | 3 | 5 | Edge1:2, Edge2:15, Central:50
Config 2 | 20 Mbps | 5 | 15 | Edge1:2, Edge2:15, Central:50
Config 3 | 10 Mbps | 5 | 15 | Edge1:2, Edge2:15, Central:50

## Slide 12
Network Actions and Data Collection
4
1. Autoscale Limit
Horizontal scaling: increase/decrease number of replicas (pods) in K8 clusters.
3. Change Priority
Adjust priority levels for both CV and URLLC UEs to control airlink bandwidth sharing.
2. Move UEs
Migrate UE context between Edge-1, Edge-2, and Central clusters.
Result
892 graphs with 11,000+ UE records.
UE Level: MBR, priority, service type, throughput, latency, packet loss, QoE
Network Level: Link configuration (latency, capacity, loss), gNB ID, attached UEs
Cluster Level: Deployed site, URLLC flavour, replicas, CPU load, served UEs
Collected Features

## Slide 13
Proposed Method
5
Figure. Flow diagram of the proposed dual-branch framework for bearing fault diagnosis.

## Slide 14
GNN Model Architecture and Training Process
4
Step 1: Enable Trace System
└─ Generate desired outputs from network emulator
Step 2: Collect Raw Data
└─ Store in table format: KPIs, topology, configurations
Step 3: Data Preprocessing
├ Convert to graph format
├ Normalize features (0-1 range)
├ Filter outliers (throughput < 50 Kbps)
└─ Result: 892 valid graphs
Step 4: Train/Test Split
└─ 80% training / 20% testing
Step 5: Model Training & Evaluation
└─ Train GNN and evaluate on test set
5-Step Training Pipeline
Model Parameters
Parameter | Value
Embedding size | 64
Layers | 4
Aggregation | sum
Learning rate | 0.001
Dropout probability | 0.3
Optimizer | Adam
Readout Function: MLP (Multi-Layer Perceptron)
Activation Function: ReLU
Update Function: Feedforward NN
Design Choices

## Slide 15
GNN Training Process
4
Step 1: DATA PREPARATION
├─ Convert network snapshots to graphs
├─ Normalize all features to [0, 1]
├─ Filter outliers (throughput < 50 Kbps)
└─ Result: 892 clean graphs
Step 2: DATA SPLITTING
├─ 80% training graphs
├─ 20% testing graphs
└─ Separate holdout configuration
Step 3: TRAINING LOOP (300 epochs)
├─ For each batch of 32 graphs:
│ ├─ Forward pass (message passing)
│ ├─ Compute predictions
│ ├─ Calculate RMSE loss
│ ├─ Backpropagation
│ └─ Update weights (Adam optimizer)
└─ Monitor training and validation loss
Step 4: EVALUATION
├─ Test on holdout configuration
├─ Calculate MAPE, RMSE
└─ Compare with baseline
Training Process
Key Design Choices
Heterogeneous graph: Different node types
4 layers: Captures 4-hop neighborhoods
SUM aggregation: Accounts for total load
Dropout 0.3: Prevents overfitting
ReLU activation: Non-linear learning
Adam optimizer: Adaptive learning rate
RMSE loss: Penalizes large errors more

## Slide 16
GNN Training Process
4
Fig. CDF of prediction errors by the baseline neural network.
Fig. CDF of prediction errors by the GNN agent.

## Slide 17
GNN Training Process
4
Fig. Measured and predicted latency for sample graphs.
Fig. CDF of prediction errors on holdout datasets

## Slide 18
Why Does GNN Generalize Better?
4
1. Topology-Aware Learning
GNN learns from graph structure, capturing relationships between nodes (UEs, gateways, clusters) regardless of specific configuration.
2. Message Passing Mechanism
Information propagates through network topology, mimicking actual signal flow in real networks.
3. Permutation Invariance
GNN output is independent of node ordering, making it robust to different network configurations.
4. Shared Parameters
Same update functions applied across all nodes of same type, enabling transfer to different scales.
Baseline NN Limitation
Traditional NNs treat each UE's features independently without considering network topology. They cannot capture how a UE's latency is affected by other UEs competing for bandwidth or by cluster proximity.
Key Insight: GNN's ability to model network topology as a graph enables learning transferable patterns that generalize to new configurations.

## Slide 19
Key Contributions and Advantages
16
1. Novel Application of GNN in Intent-Based Networks
First work to use GNN as prediction agents within Intent Management Functions for autonomous conflict detection
2. Heterogeneous Graph Modeling Methodology
Detailed framework for modeling latency prediction as node-level regression on heterogeneous graphs (multiple node types)
3. Comprehensive Evaluation
• 55% better accuracy than baseline NN • Up to 60% better generalization to unseen configurations • Real-world validation on production-grade emulator
4. Practical Deployment Path
Demonstrates that GNN-based prediction agents are accurate (6-9% MAPE) and fast enough for real-time conflict detection
This work enables fully autonomous, zero-touch network management essential for 6G networks

## Slide 20
Conclusion
1. Problem: Intent-based networks need accurate prediction agents for conflict detection, but traditional ML approaches show poor generalization.
2. Solution: Graph Neural Networks naturally model network topology and enable accurate, scalable predictions.
3. Results: GNN achieves 6-9% MAPE (55% better than baseline) with superior generalization (up to 60% improvement).
4. Impact: Enables autonomous network management essential for 6G with zero-touch operation.
5. Significance: First application of GNN for prediction agents in Intent Management Functions, paving the way for fully autonomous networks.
16
GNNs are a promising modeling approach for network environments that enable predictions in a scalable and generalizable manner.

## Slide 21
Limitations and Challenges
16
Practical Challenges
• Integration with existing network management systems • Handling network topology changes • Model update/retraining strategy
Current Limitations
1. Single KPI Prediction: Only predicts latency; real IMF needs multiple KPIs (throughput, packet loss, QoE) simultaneously.
2. Limited-Service Scenarios: Tested only on URLLC + WebRTC; production needs diverse services (eMBB, mMTC, etc.).
3. Controlled Environment: Network emulator is simplified compared to real-world deployments with unpredictable interference.
4. Computational Overhead: GNN training and inference require more computation than simple models (though still real-time capable).
5. Data Requirements: Needs sufficient training data covering diverse configurations.

## Slide 22
Future Work
1. Multi-KPI Prediction
Extend GNN to simultaneously predict multiple KPIs (latency, throughput, packet loss, QoE) for comprehensive conflict detection
17
2. Expanded Service Coverage
Include more service types: eMBB (enhanced Mobile Broadband), mMTC (massive Machine Type Communications), AR/VR applications
3. Complete IMF Integration
Deploy multiple GNN prediction agents within full Intent Management Function and evaluate end-to-end conflict resolution capability
4. Online Learning and Adaptation
Develop mechanisms for continuous model updating as network conditions evolve without full retraining

## Slide 23
References (1/2)
[1] D. A. Temesgene, E. D. Biyar, A. Silva, A. Likhyani, and A. Zahernszky, "Graph Neural Network for Building Prediction Agents in Intent-Based Zero-Touch Networks.
[2] P. H. Gomes, M. Buhrgard, J. ," in ICC 2024 – IEEE International Conference on Communications, Denver, CO, USA, pp. 974–979, 2024. doi: 10.1109/ICC51166.2024.10622342 Harmatos, S. K. Mohalik, D. Roeland, and J. Niemöller, "Intent-driven closed loops for autonomous networks," Journal of ICT Standardization, pp. 257–290, 2021.
[3] J. Niemöller, R. Szabó, A. Záhemszky, and D. Roeland, "Creating autonomous networks with intent-based closed loops," Ericsson Technology Review, vol. 2022, no. 4, pp. 2–11, 2022.
[4] A. C. Baktir, A. D. N. Junior, A. Záhemszky, A. Likhyani, D. A. Temesgene, D. Roeland, E. D. Biyar, R. F. Ustok, M. Orlic, and M. D'Angelo, "Intent-based cognitive closed-loop management with built-in conflict handling," in 2022 IEEE 8th International Conference on Network Softwarization (NetSoft), pp. 73–78, 2022.
[5] S. He, S. Xiong, Y. Ou, J. Zhang, J. Wang, Y. Huang, and Y. Zhang, "An overview on the application of graph neural networks in wireless networks," IEEE Open Journal of the Communications Society, vol. 2, pp. 2547–2565, 2021.
[6] Y. Shen, J. Zhang, S. H. Song, and K. B. Letaief, "Graph neural networks for wireless communications: From theory to practice," IEEE Transactions on Wireless Communications, vol. 22, no. 5, pp. 3554–3569, 2023.
[7] L. Hui, M. Wang, L. Zhang, L. Lu, and Y. Cui, "Digital twin for networking: A data-driven performance modeling perspective," IEEE Network, vol. 37, no. 3, pp. 202–209, 2023.
[8] J. Skarding, B. Gabrys, and K. Musial, "Foundations and modeling of dynamic networks using dynamic graph neural networks: A survey," IEEE Access, vol. 9, pp. 79143–79168, 2021.
17

## Slide 24
References (2/2)
[9] H. Wang, Y. Wu, G. Min, and W. Miao, "A graph neural network-based digital twin for network slicing management," IEEE Transactions on Industrial Informatics, vol. 18, no. 2, pp. 1367–1376, 2022.
[10] M. Farreras, P. Soto, M. Camelo, L. Fàbrega, and P. Vilà, "Improving network delay predictions using gnns," Journal of Network and Systems Management, vol. 31, no. 4, p. 65, 2023.
[11] K. Rusek, J. Suárez-Varela, P. Almasan, P. Barlet-Ros, and A. Cabellos-Aparicio, "Routenet: Leveraging graph neural networks for network modeling and optimization in sdn," IEEE Journal on Selected Areas in Communications, vol. 38, no. 10, pp. 2260–2270, 2020.
[12] Z. Ge, J. Hou, and A. Nayak, "Gnn-based end-to-end delay prediction in software defined networking," in 2022 18th International Conference on Distributed Computing in Sensor Systems (DCOSS), pp. 372–378, 2022.
[13] P. Larrenie, J.-F. Bercher, O. Venard, and I. Lahsen-Cherif, "Low complexity approaches for end-to-end latency prediction," in 2022 13th International Conference on Computing Communication and Networking Technologies (ICCCNT), pp. 1–6, IEEE, 2022.
[14] D. S. H. Tam, Y. Liu, H. Xu, S. Xie, and W. C. Lau, "Pert-gnn: Latency prediction for microservice-based cloud-native applications via graph neural networks," in Proceedings of the 29th ACM SIGKDD Conference on Knowledge Discovery and Data Mining, KDD '23, (New York, NY, USA), p. 2155–2165, Association for Computing Machinery, 2023.
[15] T. A. Khan, A. Muhammad, W. Akbar, A. Mehmood, A. Rafiq, and W.-C. Song, "Intent-based networking approach for service route and qos control on koren sdi," in 2021 IEEE 7th International Conference on Network Softwarization (NetSoft), pp. 24–30, 2021.
[16] A. Romero-Garcés, A. Hidalgo-Paniagua, M. González-García, and A. Bandera, "On managing knowledge for mape-k loops in self-adaptive robotics using a graph-based runtime model," Applied Sciences, vol. 12, no. 17, p. 8583, 2022.
17

## Slide 25
Thank You
18